## Slide 1
  TANGO - WP1
ATTIVITA’ DI RICERCA NEL PERIODO
DICEMBRE 2002- GIUGNO 2003

## Slide 2: CNR-ISTI ACTIVITY SUMMARY
Optimization of TCP goodput for connections over links with at least one wireless hop (generalities)
Criteria followed to maximize TCP goodput of a wireless connection with random packet loss acting on transmission parameters, given a channel quality condition
Models/simulation tools adopted to evaluate the goodput of a TCP connection (WP2)
Results achieved for long range connections over geostationary satellite links corrupted by additive white Gaussian noise (AWGN)
Future activity

## Slide 3: Optimization of TCP connections over wireless links (1 out of 3)
The end-to-end throughput of a TCP connection (goodput) depends, among other factors, on rate and modality of packet loss at IP level
Packet loss due to corruption over low quality wireless channels may dramatically reduce goodput, especially on high delay-bandwidth product channels
In wireless links, given a transmission power, spectrum occupancy and antennas’ characteristics, BER can be improved acting on modulation scheme and FEC
In general, BER can be reduced at the cost of a lower bit rate (TCP bottleneck rate)
Problem: to maximize TCP goodput acting on modulation scheme and FEC

## Slide 4: Optimization of TCP connections over wireless links (2 out of 3)
TCP goodput in packets/s is practically given by the product of the bottleneck rate by a decreasing function of the packet loss and thus of the BER
BER is an increasing function of bottleneck rate
Maximization of goodput is obtained by trading bottleneck rate for data quality
This is made for each channel quality condition, characterized by C/N0 (carrier power over one sided noise spectral density) ratio, in AWGN presence
We propose to choose the vector of transmission parameters which yield maximum goodput for each channel condition instead of applying general rules (e.g. BER thresholds)

## Slide 5: Optimization of TCP connections over wireless links (3 out of 3)
For each channel condition max TCP goodput is obtained with transmission parameters that give minimum BER for the same information bit rate (Circled points in the figure)

## Slide 6: TCP THROUGHPUT EVALUATION TOOLS Steady state analysis of long run connections
ASSUMPTIONS:
Reno TCP implementation without the SACK option
Window Scale option used (RFC 1185)
rwnd is never a limiting factor and transmission window equal to the congestion window cwnd
Packet loss detection on receiving three duplicate ACKs, never because of a timeout
Transmitting side never runs out of data to transmit
Steady state analysis, limited to Congestion Avoidance phase
A buffer of capacity B is associated with the bottleneck link, whose transmission rate is  segments/s.
Independent packet losses (AWGN channel)

## Slide 7: TCP THROUGHPUT EVALUATION TOOLS
Modification of the approximate analysis is made by T. V. Lakshman and U. Madhow( “The performance of TCP/IP for networks with high bandwidth-delay products and random loss”, IEEE/ACM TON, Vol. 5, No. 3, June 1997, pp. 336-350)
  It gives slightly better results for some input conditions
  Illustrated in: N. Celandroni, F. Potortì, "Maximising single connection TCP goodput by trading bandwidth for BER", IJSC Vol. 16, pp. 63-79, 2003
TCP goodput evaluation program (TGEP) written in MathematicaTM
  Mid way between analysis and simulation
  Illustration (see WP2)

## Slide 8
Payload TCP throughput
versus segment size for
different BERs
OPTIMUM PACKET LENGTH

## Slide 9: Results of point by point optimization in a real case (1)

## Slide 10: Results of point by point optimization in a real case (2)

## Slide 11: CONVOLUTIONAL ENCODER/VITERBI DECODER CHARACTERISTICS
BER and average
error burst length
versus Ec/No for
different values of
convolutional
coding rate.
Extrapolated values
are circled.

## Slide 12
TCP throughput versus C/N0, for the complete set of transmission parameters for R = 2.048 Mbit/s. 1000 byte segments

## Slide 17
Segment Error Rate (SER) versus Eb/N0 for different convolutional coding rates and for concatenated RS(255,223)/convolutional codes, with and without symbol interleaver. 1115 byte segments

## Slide 18: Comparison of maximum throughput versus C/No for different coding types. 1115 byte segments

## Slide 19: Future activity
Analysis of erasure and erasure+convolutional coding in AWGN environment
Analysis of multi-connections sharing the same AWGN link
  Different latency values
  Different segment lengths
  Different data protections
Analysis of short connections
  Single and multi-connections per link
  Long + short connections over the same link
Analysis in wireless environments
  Correlated packet losses (multipath fading)
  Impact of Wi Fi MAC protocols

## Slide 20: REFERENCES
1. C. Partridge and T. J. Shepard, “TCP/IP performance over satellite links”, IEEE Network, Vol. 11, No. 5,
September/October 1997, pp. 44-49
2. N. Celandroni, F. Potortì, "Maximising single connection TCPgoodpu by trading bandwidth for BER",
IJSC Vol. 16, pp. 63-79, 2003.
3. T. V. Lakshman and U. Madhow, “The performance of TCP/IP for networks with high bandwidth-delay
products and random loss”, IEEE/ACM Trans. on Networking, Vol. 5, No. 3, June 1997, pp. 336-350.
4. M. Allman, V. Paxson and W. S. Stevens, “TCP congestion control”, RFC 2581, April 1999.
5. “Q1401: K=7 rate 1/2 single-chip Viterbi decoder technical data sheet”, Qualcomm incorporated, September 1987.
6. P. Karn, “Error correcting codes”,
<URL:http://people.qualcomm.com/karn/code/fec/>.
7. V. Jacobson, R. Braden and D. Borman, “TCP extensions for high performance”, IETF, RFC 1323, May 1992.
8. E. Altman, K. Avrachenkov, C. Barakat, “A stochastic model of TCP/IP with stationary random losses”,
Computer Commun. Review, Vol.30, No.4, October 2000, pp. 231-242.
9. M. K. Simon, J.K. Omura, R. A. Scholtz and B. K. Levitt, "Spread Spectrum Communications Handbook",
revised edition: McGraw-Hill, 1994.
10. M. Riley and I. Richardson, "Reed_Solomon Codes", online at
  http://www.4i2i.com/reed_solomon_codes.htm, November 2002.
11. R. Blahut, "Theory and Practice of Error Control Codes", Reading, MA: Addison-Wesley, 1983.
12. S. Lin and D.J. Costello, "Error Control Coding: Fundamental and Applications": Prentice-Hall, 1983.