## Slide 1: A Simple Markovian Approach to Model Internet Traffic at Edge Routers
Luca Muscariello
Michela Meo
Marco Mellia
Renato Lo Cigno
Marco Ajmone Marsan

## Slide 2: Followed Approach
Measure
Collect all IP
packets
Data analysis
Statistics
definition
Parameters
inference
Traffic rate,
time series, Hurst...
Markovian model
Definition and
validation

## Slide 3: Network Analysis Tools: TSTAT- TCP STatistic and Analysis Tool
Example of computed statistics for TCP:
  flow length distribution
  congestion/receiver window size
  out-of-sequence segments
  duplicated segments
  RTT estimates
Tstat reads all IP headers flowing through the link
Distinction is made between clients and servers, and between incoming and outgoing packets/flows
Tstat rebuilds TCP flows from packets

## Slide 4
Statistics
Different time series based on the measurement time window
  10ms
  100ms
  1s
Two Time Series in a time window:
Packet Level (no. of IP packets per time unit)
TCP Level (no. of TCP flows per time unit)
Peak and Night periods have been considered

## Slide 5
Estimation of H :
TCP Flow Level and IP Packet Level
0.747
Arr100
0.736
Iarr
0.757
Arr1000
0.741
Arr10
H
Peak’01
Already known results: LRD at both TCP and IP levels
0.873
Arr100
0.867
Iarr
0.880
Arr1000
0.883
Arr10
H
Peak’01
TCP
IP

## Slide 6: Markovian Model
Poisson session arrivals
Number of flows within a session is Geometric
Interarrival time of flows within a session is neg. exponential
Number of packets within a flow is geometric
Interarrival time of packets within a flow is neg. exponential

## Slide 7: State-Transition Diagram
0,0
1,0
2,0
0,1
1,1
2,1
0,2
1,2
2,2
0,3
1,3
2,3
. . .
. . .
. . .
. . .
. . .
. . .
. . .
State definition:
S = ( Nf, Ns)
The memory of the model depends on the number of active flows and sessions
The session dynamic is slower than the flow one and tends to be responsible of correlation over large scales

## Slide 8: Model Parameters
The model has 5 parameters
Session arrival rate s
Flow arrival rate within a session fs
Packet arrival rate within a flow pf
Number of flows per session Nfs
Number of packets per flow Npf
3 parameters are directly estimated from the measured mean
number of packets per flow
rate of packets in a flow
rate of flows
2 parameters are used to fit long term correlation
C= s/fs
Nfs
related to the duration and traffic of a session
Notes: C e’ il rapporto tra arrivi delle sessioni e dei flussi per sessione (C alto flussi nella sessione meno ravvicinati)
Nfs num di flussi per sessione

## Slide 9: Parameters Sensitivity
1
Nfs
0,5
0,6
0,7
0,8
0,9
5
10
15
20
25
30
35
40
45
Hf
0,5
0,6
0,7
0,8
0,9
1
5
10
15
20
25
30
35
40
45
Nfs
Hp
C=1
C=2
C=4
C=1
C=2
C=4

## Slide 10: MMPP Definition: Infinitesimal Generator
State definition: S = ( Nf, Ns)
Q is infinite-size and has a block-structure
Each block is infinite-size
For numerical analysis the matrix need to be truncated (this is a critical issue)

## Slide 11: Queue Performance: Peak’01
10
0
10
1
10
2
10
3
10
4
10
5
10
-4
10
-3
10
-2
10
-1
10
0
x
P(X=x)
P(X=x)
Real Trace
MMPP
Poisson
10
-4
10
-3
10
-2
10
-1
10
0
10
0
10
1
10
2
10
3
10
4
10
5
x
P(X=x)
P(X=x)
10
-4
10
-3
10
-2
10
-1
10
0
10
0
10
1
10
2
10
3
10
4
10
5
x
10
-4
10
-3
10
-2
10
-1
10
0
10
0
10
1
10
2
10
3
10
4
10
5
x

## Slide 12: Queue Performance: Night’01
0
1
2
3
4
5
P(X=x)
0
1
2
3
4
5
Real Trace
MMPP
Poisson
10
-4
10
-3
10
-2
10
-1
10
0
P(X=x)
10
-4
10
-3
10
-2
10
-1
10
0
10
0
10
1
10
2
10
3
10
4
10
5
x
10
0
10
1
10
2
10
3
10
4
10
5
x
0
1
2
3
4
5
-4
-3
-2
-1
0
P(X=x)
-4
-3
-2
P(X=x)
10
0
10
1
10
2
10
3
10
4
10
5
x
10
-4
10
-3
10
-2
10
-1
10
0
10
0
10
1
10
2
10
3
10
4
10
5
x
10
-4
10
-3
10
-2
10
-1
10
0

## Slide 13: Finite Buffer Queue
10
0
10
-4


P(X=x)
x
512
256
128
64
32
Real Trace
MMPP
Poisson
10
-3
10
-2
10
0
10
-1
10
2
10
1
10
3

## Slide 14: Conclusions
We proposed a model of real traffic which is accurate in the considered simple network scenarios
The traffic generator is simple to fit and the parameters are related to the hierarchical structure of real traffic
The model fitting procedure tries also to take into account the LRD properties of IP traffic

## Slide 15: Ongoing Research and Open Issues
Analytical and numerical results based on matrix analytic approaches
Rules to truncate the infinitesimal generator matrix Q
New more complex testing scenarios to be implemented in ns-2 (for modeling the background traffic for TCP performance purposes)